Foam Construction
============================
The folder ''FoamConstruction'' contains two files: ''SpherePackFB.exe'' and ''FoamGeometryConstruction_Periodic.py''. The ''SpherePackFB.exe'' is called to be executed in ''FoamGeometryConstruction_Periodic.py''. So to execute the code you need to have ''SpherePackFB.exe'' and ''FoamGeometryConstruction_Periodic.py'' in a same directory.
The input variables are: ''MU'' and ''SIGMA'' which are mean and standard deviation values for cell size distribution and also ''NumOfCells'' which represents the number of cells required to have in final representative volume element (RVE). All these inputs can be adjusted by modifying lines 5, 6 and 7 in ''FoamGeometryConstruction_Periodic.py''. By default: ''MU=0.15'' , ''SIGMA=0.30'' and ''NumOfCells=100''.
 ''FoamGeometryConstruction_Periodic.py'' creates several files as outputs:
1- ''PeriodicRVE.geo'' which is the periodic geometry of foam in .GEO format.
2- ''CellVolumes_PeriodicRVE.txt'' containing the volumes of all the cells in RVE.
3- ''FaceAreas_PeriodicRVE.txt'' containing the areas of all the faces in RVE.
4- ''EdgeLengths_PeriodicRVE.txt'' containing the lengths of all the edges in RVE.
5- ''HyperMeshinput.cmf'' which is a input file for ''Hypermesh'' to recreate the geometry.

Requirements for running:

1- NEPER installed. NEPER could be downloaded through: ''http://neper.sourceforge.net/ ''
2- ''wine software'' to have ability of running executable files (i.e. file.exe).